## Slide 1: Fire Prevention

## Slide 2: Introduction
This is the Fire Triangle. It’s a tetrahedron because there are four elements that MUST be present for a fire to exist. There must be Oxygen to sustain combustion, Heat to raise the material to its ignition temperature, Fuel to support the combustion and a Chemical Reaction between the other three elements.
Remove any one of the four elements to extinguish the fire.
The concept of Fire Prevention is based upon keeping these four elements separate.

## Slide 3: Types of Fires
Class A – fires in ordinary combustibles, such as wood, paper, cloth, trash and plastics
Class B – fires in flammable liquids, such as gasoline, petroleum oil, and paint.

## Slide 4: Types of Fires
Class C – fires involving electrical equipment, motors, transformers and appliances.
Class D – fires in combustible metals such as potassium, sodium and aluminum
Class K – fires in cooking oils, greases, animal fats and vegetable fats.

## Slide 5: Types of Fire Extinguishers
Water and Foam
  Extinguish the fire by taking aware the Heat element
  Class A fires only
Carbon Dioxide
  Extinguish the fire by taking aware the Oxygen element
  Class B & C fires only

## Slide 6: Types of Fire Extinguishers
Dry Chemical
  Extinguish the fire by interrupting the chemical reaction of the fire triangle
  Today’s most widely used type of fire extinguisher
  Effective on Class A, B, and C fires
  Creates a barrier between the oxygen and fuel elements

## Slide 7: Types of Fire Extinguishers
Wet Chemical
  Extinguishes the fire by removing the heat of the fire triangle and prevents re-ignition
  Developed for modern, high efficiency deep fat fryers in commercial cooking operations

## Slide 8: Types of Fire Extinguishers
Clean Agent
  Include Halon agents and less ozone depleting halocarbon agents
  Extinguish the fire by interrupting the chemical reaction of the fire triangle
  Primarily used for Class B & C fires

## Slide 9: The Rules for Fighting Fires
Just remember the three A’s
  Activate – the building alarm system or notify the fire department by calling 911, or have someone else do this for you
  Assist – any persons in immediate danger, or those incapable on their own, to exit the building, without risk to yourself
  Only after these two are completed, should you Attempt to extinguish the fire

## Slide 10: Only Fight a Fire
IF the fire is small and contained
IF you are safe from toxic smoke
IF you have a means of escape
IF you instincts tell you it’s OK

## Slide 11: Fire Extinguisher Use
It is important to know the locations and the types of extinguishers in your workplace prior to actually using one.
Fire extinguishers can be heavy, so practice picking up and holding an extinguisher
Read the operating instructions
Practice releasing the discharge hose

## Slide 12: P A S S*
PULL the pin
AIM the nozzle or hose at the base of the fire from the recommended safe distance
SQUEEZE the operating lever to discharge the fire extinguisher agent
Starting at the recommended distance, SWEEP the nozzle or hose from side to side until the fire is out
  Move forward or around the fire area as the fire diminishes
  Watch the are in case of re-ignition
* Water and Foam extinguisher

## Slide 13: Fire Extinguisher Inspection
Fire extinguishers must be inspected or given a “quick check” every 30 days and answer 3 questions…
  Is the extinguisher in the correct location?
  Is it visible and accessible?
  Does the gauge or pressure indicator show the correct pressure?

## Slide 14: Fire Extinguisher Maintenance
Fire extinguishers must be maintained annually by a fire equipment professional
Maintenance includes recharge of materials, parts, and lubricants
www.fireextinguisher.com

## Slide 15: Test
T F The four elements that must be
present for fire exist include heat, oxygen, fuel and a chemical reaction between the three.
2. T F The concept of fire prevention is to
keep these elements separate.
T F There are four classes of fire. Class A,
B, C and K

## Slide 16: Test
4. T F Class B fires are those that occur
involving paper and wood.
5. T F Multipurpose dry chemical
extinguishers are effective on all
classes except D and K fires.
T F To remember the rules of fighting
fires, just remember the three A’s:
Activate Assist and Attempt

## Slide 17: Test
T F The four simple steps or operating a
fire extinguisher can be remembers
with the word PASS. Pull, Activate,
Squeeze, Sweep
T F After the fire has been extinguished,
it is important to watch the site for
re-ignition.
T F Fire extinguishers must be inspected or
checked every 60 days.

## Slide 18: Test
T F According to CARF, local, state, and
national codes and regulations, fire
extinguishers must be maintained bi-
annually.